## Slide 1: ENEL 895AK
Hierarchical Self-Certified Key Management

## Slide 2: Hierarchical Self-Certified Management
[2] proposes a cluster-based system for establishing secure sessions between cluster heads and members with no prior shared knowledge
This system was proposed for medical sensor network applications
This system depends on a tree-based hierarchy system and is based on setting up Shared Session Keys (SSK) between cluster heads and members
The system has a root level Secure Access Point (SAP) which acts as the WSN gateway. The root SAP manages other cluster head SAP’s in the backbone cluster. These cluster head SAP’s in turn manage nodes in their cluster.
C. H. Tseng, S. Wang and W. Tsaur, "Hierarchical and Dynamic Elliptic Curve Cryptosystem Based Self-Certified Public Key Scheme for Medical Data Protection," in IEEE Transactions on Reliability, vol. 64, no. 3, pp. 1078-1085, Sept. 2015.

## Slide 3: Architecture of the System
The Root SAP manages all cluster heads in the Backbone Cluster
Each cluster head SAP is responsible for an area cluster
The SAP’s drive session creation and management
Each SAP has a pre-established SSK with the Root
Each Node dynamically creates a new SSK with their SAP when needed

## Slide 4: Setup and Registration Phase
Network setup consists of nodes registering with a cluster head (CH) to become cluster members (CM)
The registration phase is used to let the CH know about the new CM and to derive a public/private key pair for the CM to use
  The key pair is built using the CM’s master key and the CH’s private key
  This process allows the CH to derive the public key of the CM
  It also allows the CM to derive the private key without the CH having access to it
The CH manages sessions for its cluster, and the CMs send data through the CH inside these sessions

## Slide 5: Node Registration
ML - Master Key
ID - Node ID
RT - Registration Token
WT - Witness Token
PK - Public Key
SK - Private Key
RREQ - Registration Request
RREP - Registration Response

## Slide 6: Deriving Key Pairs
The node begins by crafting a RREQ:
  It generates a Registration Token using its Master Key and ID:
  It sends RTCM and IDCM in the RREQ to the CH
The CH receives the RREQ:
  It generates a random Registration Number RNCH and uses it to derive PKCM:
  It then stores PKCM in its cluster key database for use later

## Slide 7: Deriving Key Pairs
Then the CH crafts a RREP packet:
  It generates a Witness Token using its Key, ID, and the Registration Number:
  It sends WTCH and PKCM in the RREP to the CM
The CM receives the RREP:
  It derives its private key SKCM:
  And verifies it:

## Slide 8: Communication Phase
A communication is initiated by the CM by sending a SREQ packet
The first step in communication is the CM and CH setting up a Shared Session Key (SSK), which is a one-time shared secret:
  The SSK is derived using the previously established public/private key pair
  The SSK can be derived without the CM having to send or store its own public key
  This helps reduce data transmitted by the CM which is a lower function node
This way, the CM only needs to share it’s ID and a Time Token with the CH, then use the returned Session Token and its private key to derive the SSK

## Slide 9: Shared Session Key
TT - Time Token
ID - Node ID
PK - Public Key
SSK - Shared Session Key
SREQ - Session Request
SREP - Session Response

## Slide 10: Deriving Shared Session Key
The CM begins by crafting a SREQ:
  It generates a Time Token using a time-variant Session Number:
  It sends TTCM and IDCM in the SREQ to the CH
The CH receives the SREQ:
  Using the IDCM, the CH looks up the CM’s public key in its database
  It then generates a time token using a time-variant Session Number:
  It sends TTCH, IDCH, and its public key PKCH in the SREP to the CM

## Slide 11: Deriving Shared Session Key
The CH derives a Session Token STCH and the SSK as:
The CH derives a Session Token STCM and the SSK as :
Now both parties have derived the same Shared Session Key

## Slide 12: Testing
The protocol was implemented on the following testbed:
  The Root SAP was a CPU connected to a cloud server using Ethernet and connected to a Zigbee network using a USB dongle
  The SAP’s were Beaglebone boards running a Linux container with a USB dongle used to access the Zigbee network
  The cluster members were Beaglebone boards running a Linux container, with an SD card interface used for storage and a USB dongle used to access the Zigbee network
The testbed used an ECG dataset stored on the SD cards on each node to simulate real medical data in the network

## Slide 13: Results – Network Performance
Network Overhead:
  By limit unnecessary sending of public keys, message overhead is reduced across the network
Network Delay:
  By deriving key pairs and session keys without modular exponentiation, the registration phase and the session setup phase are both faster than an equivalent RSA implementation by a factor of
Security
  By deriving key pairs based on the nodes master key, the private key is never revealed to any outside parties
  Security of the SSK is equivalent to the security of the master key
  The system is based on ECC, so a 160bit master key corresponds to the same security as RSA 1024

## Slide 14: Results – Cluster Member
The results show significantly less overhead than a comparable RSA 1024 protocol
As the number of parallel sessions in the network increases, the overhead savings increase
Message overhead in an area cluster

## Slide 15: Results – Cluster Head
As can be expected, the message overhead per Cluster head decreases as clusters are added
The change in savings per SAP decreases as more SAP’s are added
  This is due to smaller area clusters being formed
  This tends to zero as the number of SAP’s approaches the number of nodes
Message overhead per Cluster Head based on 60 Nodes

## Slide 16: References
C. H. Tseng, S. Wang and W. Tsaur, "Hierarchical and Dynamic Elliptic Curve Cryptosystem Based Self-Certified Public Key Scheme for Medical Data Protection," in IEEE Transactions on Reliability, vol. 64, no. 3, pp. 1078-1085, Sept. 2015.