## Slide 1: ENEL895AK
Side Channel Attacks
Brant Geddes

## Slide 2: Cryptanalysis – Breaking Encryption
Linear cryptanalysis is based on solving a system of equations to recover portions of the key. Most block ciphers have a non-linear element, such as the S-block in DES, inserted to make this more difficult [3]
Differential Cryptanalysis looks for patterns and attempts to recover the plaintext from those patterns
Side-Channel Attacks look for patterns in secondary variables rather than directly attacking the ciphertext. Secondary variables could include:
  Power consumption (Power Differential Attacks) [1]
  Time (Spectre Attacks) [2][3]
  Cache Storage [4]
  Electromagnetic Leakage (Tempest Attacks) [5]

## Slide 3: Side-Channel Attacks
Side-Channel Attacks use information available outside of the cipher operation to either transform the ciphertext to plaintext, learn the keys and initializing vectors in use, or learn the plaintext data before it is encrypted.
Side-Channel Attacks are usually statistics based and rely on having enough data to pull meaningful information out
Many of these attacks require physical access (Power Differential), or require that the attacker be in the vicinity (Tempest). Others can be accomplished remotely or through the use of a proxy (Timing Attacks, Sound Analysis, Fault Analysis)

## Slide 4: Power Differential Attacks
Power Differential Attacks attempt to find a statistical correlation between differences in power drawn during an operation and the operands.
Typically, physical access to the device or circuit is required and a oscilloscope and computer are required to analyze the information.
In addition, the attacker generally requires the ability to obtain plaintext/cyphertext pairs alongside the time-series power consumption during encryption
M. Safta, P. Svasta, M. Dima, A. Marghescu and M. Costiuc, "Design and setup of Power Analysis attacks," 2016 IEEE 22nd International Symposium for Design and Technology in Electronic Packaging (SIITME), Oradea, 2016, pp. 110-113.

## Slide 5: Timing Attacks
Timing Attacks generally aim to take advantage of variations in time to encrypt to recover the key from a large set of cyphertexts and their corresponding encryption times.
Several factors can add to the variability of an encryption algorithm, such as:
  Branching
  Cache Hits and Misses
  Non-Constant Processor Instructions (Pipeline Bubbling)
  Compiler Optimizations
E. English and S. Hamilton, "Network security under siege: the timing attack," in Computer, vol. 29, no. 3, pp. 95-97, March 1996

## Slide 6: Cache Attacks: Spectre
Modern processors use an optimization called Speculative Execution, which performs work before it is needed. This optimization trains the CPU to lookahead and pre-compute possible values when it can.
The above code is a possible target of Speculative Execution
  If x is within the correct array size bounds, the CPU will branch inside the IF
  If this happens often, the CPU will start to pre-compute the results of y
  If x is outside the correct array size bounds, the CPU will throwaway it’s precomputed value
P. Kocher et al., "Spectre Attacks: Exploiting Speculative Execution," 2019 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA, 2019, pp. 1-19

## Slide 7: Cache Attacks: Spectre
The Spectre attack leverages this optimization and the fact that commonly used values end up in the CPU’s cache.
If an attacker can game the Speculative Execution Optimization, they can move sensitive data to the CPU’s cache
Even though the CPU has thrown the pre-computed value away, it remains in the cache until it is overwritten
This method can be combined with direct access to the cache or a timing attack to recover sensitive information such as keys or plaintext
P. Kocher et al., "Spectre Attacks: Exploiting Speculative Execution," 2019 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA, 2019, pp. 1-19
J. Kong, O. Aciicmez, J. Seifert and H. Zhou, "Architecting against Software Cache-Based Side-Channel Attacks," in IEEE Transactions on Computers, vol. 62, no. 7, pp. 1276-1288, July 2013

## Slide 8: EM Leakage Attacks: Tempest
Electromagnetic Leakage Attacks read EM radiation leaked from the target device to attempt to recover sensitive information.
This EM leakage can be read from many sources such as:
  Electronic Memory
  Hard Drives
  Interface Devices (Monitor, Keyboard, Mouse)
  Wireless or Wired Networking Devices and Lines
A Tempest Attack reads this radiation and recovers sensitive data from it:
  Experiments done in [5] on a typical i7 processor show that this information can be recovered from as far away as 1.6 meters and require as little as an antenna and a powerful processor for data analysis
A. Zajić and M. Prvulovic, "Experimental Demonstration of Electromagnetic Information Leakage From Modern Processor-Memory Systems," in IEEE Transactions on Electromagnetic Compatibility, vol. 56, no. 4, pp. 885-893, Aug. 2014.

## Slide 9: Fault Attacks
Fault attacks leverage error handling in hardware, software, protocols, or algorithms to determine information.
Common faults include handling data that is too large or out of range, changing system parameters of a processor such as voltage and frequency, or memory/cache glitches
These attacks can have consequences ranging from giving an attacker inside information such as decision bounds, to directly recovering secret information such as keys or plaintext, and even elevation of privilege or local access to a machine.
M. Bishop, S. Engle, D. Howard and S. Whalen, "A Taxonomy of Buffer Overflow Characteristics," in IEEE Transactions on Dependable and Secure Computing, vol. 9, no. 3, pp. 305-317, May-June 2012.
D. Page and F. Vercauteren, "A Fault Attack on Pairing-Based Cryptography," in IEEE Transactions on Computers, vol. 55, no. 9, pp. 1075-1080, Sept. 2006.

## Slide 10: Fault Attacks - Examples
A common form of fault attack is a Buffer Overflow Exploit:
  If application software doesn’t properly check data size before processing it, a large string or array can cause a buffer overflow to happen
  A portion of the data can overflow into executable code space
  Malicious instructions can be included in the data and can be executed if carefully planned, causing an attacker to be able to execute any code they want on a secure system
Another form of fault attack can be seen in [7], which breaks an RSA implementation (Duursma-Lee) by introducing a fault that changes a bound in the algorithm. This allows the attacker to recover the private key
M. Bishop, S. Engle, D. Howard and S. Whalen, "A Taxonomy of Buffer Overflow Characteristics," in IEEE Transactions on Dependable and Secure Computing, vol. 9, no. 3, pp. 305-317, May-June 2012.
D. Page and F. Vercauteren, "A Fault Attack on Pairing-Based Cryptography," in IEEE Transactions on Computers, vol. 55, no. 9, pp. 1075-1080, Sept. 2006.

## Slide 11: Attacking Side-Channels in ECC
ECC implementations are also vulnerable to Side-Channel Attacks
Work done in [8] show that ECC implementations built on a reduced set of elliptic curves called Koblitz Curves are susceptible to Power Differential Attacks
  This method attempts to correlate private key information to the power drawn when performing various operations. (ie. The paper states that power consumption differences while point doubling are directly correlated to the hamming weight of the point)
Other attacks are possible as well, as can be seen in [9]:
  Timing attacks due to RAM hits/misses and branches can be analysed
  Other forms of Power Differential Attacks
  Fault based attacks such as buffer overflow can be used to recover sensitive information
M. A. Hasan, "Power analysis attacks and algorithmic approaches to their countermeasures for Koblitz curve cryptosystems," in IEEE Transactions on Computers, vol. 50, no. 10, pp. 1071-1083, Oct. 2001.
J. Fan, X. Guo, E. De Mulder, P. Schaumont, B. Preneel and I. Verbauwhede, "State-of-the-art of secure ECC implementations: a survey on known side-channel attacks and countermeasures," 2010 IEEE International Symposium on Hardware-Oriented Security and Trust (HOST), Anaheim, CA, 2010, pp. 76-87.

## Slide 12: Breaking ECC: Fault Analysis
An simple example of a user level stack used in a ECC encryption process can be seen below:
A theoretical attack on this algorithm could be accomplished if the size of the inputs are not checked before processing them.
A malicious user could attempt to inject code into the code space with the intent of having it return the private key
This can be stopped by proper bounds checking in the algorithm, which isn’t always done properly

## Slide 13: References
M. Safta, P. Svasta, M. Dima, A. Marghescu and M. Costiuc, "Design and setup of Power Analysis attacks," 2016 IEEE 22nd International Symposium for Design and Technology in Electronic Packaging (SIITME), Oradea, 2016, pp. 110-113.
E. English and S. Hamilton, "Network security under siege: the timing attack," in Computer, vol. 29, no. 3, pp. 95-97, March 1996
P. Kocher et al., "Spectre Attacks: Exploiting Speculative Execution," 2019 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA, 2019, pp. 1-19
J. Kong, O. Aciicmez, J. Seifert and H. Zhou, "Architecting against Software Cache-Based Side-Channel Attacks," in IEEE Transactions on Computers, vol. 62, no. 7, pp. 1276-1288, July 2013
A. Zajić and M. Prvulovic, "Experimental Demonstration of Electromagnetic Information Leakage From Modern Processor-Memory Systems," in IEEE Transactions on Electromagnetic Compatibility, vol. 56, no. 4, pp. 885-893, Aug. 2014.
M. Bishop, S. Engle, D. Howard and S. Whalen, "A Taxonomy of Buffer Overflow Characteristics," in IEEE Transactions on Dependable and Secure Computing, vol. 9, no. 3, pp. 305-317, May-June 2012.
D. Page and F. Vercauteren, "A Fault Attack on Pairing-Based Cryptography," in IEEE Transactions on Computers, vol. 55, no. 9, pp. 1075-1080, Sept. 2006.
M. A. Hasan, "Power analysis attacks and algorithmic approaches to their countermeasures for Koblitz curve cryptosystems," in IEEE Transactions on Computers, vol. 50, no. 10, pp. 1071-1083, Oct. 2001.
J. Fan, X. Guo, E. De Mulder, P. Schaumont, B. Preneel and I. Verbauwhede, "State-of-the-art of secure ECC implementations: a survey on known side-channel attacks and countermeasures," 2010 IEEE International Symposium on Hardware-Oriented Security and Trust (HOST), Anaheim, CA, 2010, pp. 76-87.